## Slide 1
Darkling Beetle
ENRICHMENT DESIGN
Jadyn Goodson-Pelayo
Bryce Dodson
Brandon Ho
Pablo Vasquez
Spring 2026 / Oklahoma City Zoo/ Engineering 1413

## Slide 2
WHY THIS MATTERS
Client
Problem Statement
OKC Zoo Information
Research
Oklahoma City Zoo
The Oklahoma City Zoo needs enrichment structures for Darkling Beetles.
  100 colonies - 57 mealworm bins
  68-72 F - 50% humidity
  Current hides: cardboard tubes and egg cartons
  Habitats- under rocks, logs, in fungi, etc.
  Nocturnal
  Like to burrow

## Slide 3
  8-10" long (small bins)
  12-15" long (large bins)
  4" wide MAX
  3-4" tall MAX
  Textured grip surface
  Ventilation holes
  Multiple entry/exit
  No wood
  Acrylic/sturdy plastic
  Non-toxic material
  No stain/paint/etc.
  Smooth edges
  $50 budget
  No small pieces
1
2
Requirements
Constraints
REQUIREMENTS, CONSTRAINTS, & DESIGN CRITERIA
3
Design Criteria
  Cleanability (30%)
  Size/Space (40%)
  Natural Look (20%)
  Elevation (10%)

## Slide 4
  Two-piece slide connection​
  8" long, 4" diameter​
  Half-cylinder log shape​
  Internal dark chambers​
  Ventilation slits (top)​
  Multiple entry/exit holes
3-D PRINTED
FIRST PROTOTYPE
ClLIENT FEEDBACK
  Add texture on bottom piece
  Add vent holes on bottom piece
  Thinner design if possible
  Make sliding easier

## Slide 5
DESIGN CHANGES
1
Fuzzy Texture
Added texture on inside and outside of bottom piece.
2
Vent Holes
Added vent holes on bottom piece floor.
3
Alignment
Added alignment grooves to help with sliding.
4
Thinner Design
Made design thinner & cheaper

## Slide 6
FINAL DESIGN
  3D printed — Brown PLA​
  Fuzzy skin texture​
  8" long × 4" diameter​
  Two-piece slide connection​
  Internal dark chambers​
  Ventilation slits (top)​
  Multiple entrances/exits​
  1.5" buried in substrate​
  Fits small & large bins​
  Washable — no hardware​

## Slide 7
PASS
PASS
PASS
PASS
PASS
PASS
PASS
PASS
PASS
TESTING & RESULTS
Requirement
Test Method
Pass Criteria
Prototype
Final
Size
Cleanable
Texture
Elevation
Ventilation
Strength
Measure/check LWH
Get dirty and attempt to wash
Place bugs; observe climbing
Place bugs; observe climbing
Dry ice fog test
Drop test
Length < 11"
Dia. < 5"
PASS
FAIL
FAIL
Does not break when dropped
Smoke exits vent holes
Bugs climb to different heights
Bugs grip and climb easy
Pieces slide apart easily

## Slide 8
CONCLUSION
KEY TAKEAWAYS
IF MORE TIME/BUDGET
  All 6 requirements passed (final design)​
  $5 total cost — 90% under budget​
  Client approved design at review​
  Fuzzy skin solved texture & elevation failures​
  Reusable, washable — replaces cardboard​
  Test additional texture patterns​
  Refine internal tunnels for burrowing​
  Produce multiple sizes for all bins​